## Slide 1
Section 3: Key Terms | 
21 Electric current | The flow of electric charge.
22 Potential difference | The potential difference between two points in an electric circuit is the work done when a coulomb of charge passes between the points. Potential difference causes charge to flow
23 Resistance | Resistance is caused by anything that opposes the flow of electric charge.
24 Charge | Anything charged that is able to move within a circuit. Electrons or ions.
25 Series | A circuit with only one route for charge to take.
26 Parallel | A circuit with only more than one route for charge to take.
Section 2: Equations to learn |  |  | 
 | Equation | Symbol equation | Units
15 | Charge flow = current x time | Q = I x t | Charge flow - coulomb (C) Current – amperes (A) Time – seconds (s)
16 | Potential difference = current x resistance | V = I x R | Potential difference – volts (V) Current – amperes (A) Resistance – ohms (Ω)
17 | Power = potential difference x current | P = V x I | Power – watt (W) Potential difference – volts (V) Current – amperes (A)
18 | Power = current2 x resistance | P = I2 x R | Power – watt (W) Current – amperes (A) Resistance – ohms (Ω)
19 | Energy transferred = power x time | E = P x t | Energy = joules (J) Power – watt (W) Time – seconds (s)
20 | Energy transferred = charge flow x potential difference | E = Q x V | Energy = joules (J) Charge flow - coulomb (C) Potential difference – volts (V)
Section 1: Circuit Symbols
Physics 2: Electricity
1
2
3
4
9
10
8
7
6
5
11
12
13
14
Section 6: The Three Core Cable | 
32 Live | Brown colour. Current flows to the appliance. Potential difference between this and other wires should be 230V.
33 Neutral | Blue colour. Current taken away from appliance. Potential difference should be 0V.
34 Earth | Yellow and green colour. Potential difference of 0V. Carries charge to Earth if live wire touches the metal casing of an appliance.
Section 5: IV Graphs
29 Fixed Resistor (Ohmic Conductor) Current and potential difference are directly proportional. Resistance is constant.
30 Filament Lamp Resistance of a filament lamp is not constant. As temperature increases, resistance increases. Ions within the lamp vibrate more, increasing collisions with electrons.
31 Diode/ LED The current through a diode flows in one direction only. The diode has a very high resistance in the reverse direction.
Section 4: V, I and R in Series and Parallel |  |  |  | 
Components connected in… |  | Current | Potential Difference | Resistance
27 | Series | The current is the same at every point in the circuit and in every component. | The total potential difference of the power supply is shared between the components. | The more resistors, the greater the resistance. The total resistance of two components is the sum of the resistance of each component. Rtotal = R1 + R2
28 | Parallel | The total current through the whole circuit is the sum of the currents through the separate components. | The potential difference across each component is the same. | Adding more resistors in parallel decreases resistance. The total resistance of two resistors is less than the resistance of the smallest individual resistor.
Section 7: Mains Electricity | 
35 Alternating Current | The current regularly changes direction e.g. mains electricity
36 Direct Current | The current flows in one direction only e.g. batteries.
37 Mains Electricity | UK mains is an alternating current of 230V and at a frequency of 50Hz.
38 National Grid | A series of cables and transformers linking power stations to consumers.
39 Step-up Transformer | Increases the potential difference for transmission across power cables. This reduces the current and therefore less heat is lost from the cables. This makes the National Grid efficient.
40 Step-down Transformer | Reduces the potential difference from the cables to 230V for use by consumers.